## Slide 1: Development and optimisation of experimental and modelling approaches to characterise high-time resolution atmospheric aerosol and its sources
PhD Student: Alice Forello
Tutor: Prof. Roberta Vecchi
End First-Year Workshop
9th October 2018

## Slide 2
Why do we care about atmospheric aerosol?
Impact on local and global scale:
Adverse human health effects
Decrease visibility
Influence the climate
Direct effect
(scattering and absorption of light)
Indirect effect
(Cloud Condensation Nuclei)
(IPCC, 2013)
Aerosol  main cause of uncertainty in total anthropogenic radiative forcing!
Notes: During breathing, these particles can enter deep in the respiratory tract and can cause…

## Slide 3
Sizes: few nm – tens m
Emissions: anthropogenic – natural ; primary – secondary
Residence times: up to several weeks
Why do we care about atmospheric aerosol?
Processes beyond aerosol emission, trasformation and removal are subject to short time scales ( hour)
High-time resolution
Directly emitted
in atmosphere
After gas-to-particle
conversion

## Slide 4
Main goal of my PhD research
High-time resolution and
size-segregated experimental data
Advanced and tailored multivariate modelling
Synergy
Assessment of
non-exhaust traffic emissions
Ultimate goal  Face an open issue:
Notes: The main goal of my PhD research is to exploit a synergistic approach to make the most of…

## Slide 5
To face the problem:
First year  Optimisation of the modelling approach
Next years  Experimental work and modelling application
Urban areas  Traffic is an important contributor to aerosol concentration in the atmosphere
Exhaust emissions
Non-Exhaust emissions:
Tyre and brake wear
Asphalt abrasion
Road dust re-suspension
Exhaust
≅ Non-exhaust!
(Amato et al., 2014)
Electric cars
? Zero aerosol emissions ?
Notes: Leggere Horvat su auto elettriche

## Slide 6
Source apportionment:
Dispersion models (deterministic)
Receptor models (statistical)
Modelling approach
Conservation of mass between emission source and receptor site
Chemical composition of environmental aerosol samples
Source apportionment
Source temporal patterns
Source chemical profiles
Input:
Output:
Notes: Sapere metodo di minimizzazione

## Slide 7
Principles of receptor modelling
X = GF + E
GOAL: Estimate source contributions at the receptor site
Factors
Sources
Physical
interpretation

## Slide 8
How is the problem solved?
 Minimization of the object function Q:
Weighed on data uncertainties
Ill-posed problem
Not a unique solution!
Addition of physical constraints
(Non-negativity; but also other a priori information)
Source of fresh sea-salt aerosol
Mg/Na = 0.12
Cl/Na = 1.8
(Bulk sea water composition from
Seinfeld & Pandis, 1998)
Simple example:

## Slide 9
Receptor modelling: state of the art
During measurement campaigns usually instrumentation with different time resolution is available
Low-time resolution
(e.g. 24 hours)
High-time resolution
(1 hour)
Advantages:
Detailed chemical speciation
Disadvantages:
Little detail of sources temporal patterns
Episodic sources not detected
Advantages:
Temporal patterns of source markers
Episodic sources
Disadvantages:
Little detail on chemical speciation
Intensive campaigns
Advanced receptor modelling
 Couple the advantages !

## Slide 10
Advanced receptor modelling: Multi-time
First implementation of Multi-time model (Zhou et al., 2004)
through Multilinear Engine 2 (ME-2) script (Paatero, 1999)
Main equation is modified to take into account experimental data with different time resolution
Sample time interval
Adjustment factors
(species replicated with different time resolution)
Research group of Milan (Crespi et al., 2016)
Implementation of:
BOOTSTRAP analysis
Constraints

## Slide 11
My contribution
 Validation of the modelling chain with a test dataset collected during my master’s degree thesis (Milan 2016)
 Entry of new metrics (optical absorption properties) for a better identification of the sources
Dataset:
Total 386 samples
22 low-time resolution variables (PM10 mass, Na, Mg, Al, Si, S, K, Ca, Cr, Mn, Fe, Cu, Zn, Pb, EC, OC, NO3-, levoglucosan, babs 405 nm, babs 532 nm, babs 635 nm, babs 780 nm)
17 hourly variables (Na, Mg, Al, Si, S, K, Ca, Cr, Mn, Fe, Cu, Zn, Pb, babs 405 nm, babs 532 nm, babs 635 nm, babs 780 nm)

## Slide 12
Results
7 factors solution
Physical interpretation:
Mm-1
Presence of chemical tracers
(e.g. Ca, Si, Al for resuspended dust)
Temporal patterns
Day and night variation; Seasonal variation
Ratio between chemical species
…etc…
Forello et al., in preparation
(2-5%)
(2-9%)
(6-12%)
(9-19%)
(12-18%)
(16-24%)
(25-42%)
Notes: Error Bars su torta

## Slide 13
Forello et al., in preparation
Levoglucosan
Fe, Cu, EC
Optical markers
Main Advantages:
New metrics: 𝛃abs at 4 wavelength (405, 532, 635, 780 nm)
Chemical markers 
Alternative to chemical markers when not available
Strengthen sources identification
No previous information on ngström Absorption Exponent (𝛂) of the source
𝛃abs∝𝛌-𝛂
Mm-1
Mm-1
Notes: Dire che non sempre disponibili chemical markers (nel primo punto dei vantaggi)
Angstrom abs exponent o abs exponent?
AGGIUNGERE INFO SU ALFA?
Mettere anche info sull’errore??Bootstrap
Error bars

## Slide 14
MODELLING:
Dataset from CARE (Carbonaceous Aerosol in Rome and Environs)  New variables (optical variables, Non-Refractory components…)
On-going work and outlook
Dataset in collaboration with research group EGAR (Environmental Geochemistry and Atmospheric Research) of the Spanish research council (CSIC) of Barcelona
Implementation and optimization of models in ME-2 script:
Real-world profiles (e.g. road dust)
Expansion of the Bootstrap analysis
Coupling different advanced approaches (e.g. different temporal resolution + different sizes)
Notes: ALTRO COMING SOON
LEGGERE TESI ALICE SU COME AMPLIARE BOOTSTRAP
I did not focus on this point because I had no time

## Slide 15
EXPERIMENTAL:
On-going work and outlook
Contribution to INFN experiment TRACCIA (Time Resolved Aerosol Characterization Challenging Improvements and Ambitions) devoted to the realization of a new high-time resolution sampler
Measurement and analysis of components of non-exhaust emissions (e.g. brake wear) in laboratory
Collaboration with EGAR group of Barcelona
(6 months abroad)
Notes: LEGGERE TESI ALICE SU COME AMPLIARE BOOTSTRAP
I did not focus on this point because I had no time

## Slide 17
(IPCC, 2013)

## Slide 18
Results
F:
ng/m3
Mm-1
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
G:
average=1
P=7
Forello et al., in preparation
Notes: Vincoli? F e EVF facile?
In realtà i babs sono in Mm-1/ng
MOSTRO DIRETTAMENTE LA SOLUZIONE CONS3

## Slide 19
INFN experiment TRACCIA
(Time Resolved Aerosol Characterization Challenging Improvements and Ambitions)
Piè di pagina: spazio libero per eventuale nome struttura o altro
First year: Experimental
Collaboration with other Italian research groups
(Florence-LABEC, Genoa, Lecce)
Design and construction of STRAS
(Size and Time Resolved Aerosol Sampler)
PM sampler with hourly resolution that resolves atmospheric aerosol in two different sizes
optimization for IBA and optical techniques
Notes: Critical issues of available similar instrumentation highlighted also during my master’s degree thesis

## Slide 20
My contribution
Study of the theoretical efficiency curves for membrane filters to be used in STRAS
Collection Efficiency =
Impaction + (2) Diffusion + (3) Direct interception
(Spurny & Lodge, 1972)
On going: STRAS prototype validation with tests at the atmospheric simulation chamber (ChAMBRe-Ge), field tests by the end of the year
 Good agreement with experimental data (within 3%)
Notes: The very first work…I won’t focus on that today…
- Mettere conti???
CHIEDERE A GIULIA E SILVIA CONFRONTO SPERIMENTALE

## Slide 22
(1) Aethalometer model (Sandradewi et al., 2008)
(2) Multi-Wavelength Absorption Analyzer model (MWAA)
(Massabò et al., 2015)
(1)
Need of a priori information on 𝛂 of sources
EC and OC apportionment is obtained with regressions/multiple regressions
0.8 – 1.1
0.9 – 2.2
babs(λ)=babs(λ)+ babs(λ)
FF
WB
babs(λ)~λ-αFF
FF
babs(λ)~λ-αWB
WB
babs(λ) = A’ λ-αFF + B’ λ-αWB
babs(λ) = A λ-αBC + B λ-αBrC
babs(λ) = A’ λ-αFF + B’ λ-αWB
(2)

## Slide 23
BOOTSTRAP:
1) Resampling and reweighting
(dataset perturbation)
2) Random rotational pulling (G solution)
Particularly stable for chemical and optical tracers (Fe, Cu, EC, 𝛃abs multi-wavelength)
TRAFFIC
 | F1 | F2 | F3 | F4 | F5 | F6 | F7 | 
F1 | 99 | 0 | 0 | 0 | 0 | 0 | 0 | 0
F2 | 2 | 93 | 2 | 0 | 0 | 0 | 0 | 2
F3 | 0 | 0 | 99 | 0 | 0 | 0 | 0 | 0
F4 | 0 | 0 | 0 | 99 | 0 | 0 | 0 | 0
F5 | 0 | 0 | 0 | 0 | 99 | 0 | 0 | 0
F6 | 2 | 0 | 2 | 0 | 0 | 95 | 0 | 0
F7 | 0 | 0 | 0 | 0 | 0 | 0 | 99 | 0